# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

EVALUATION PREPARATION	(Decontaminate Eyes)

Setup:	Evaluate this objective within a field training environment.  Gather all necessary equipment (MOPP gear, a poncho, LCE, M8 Detector Paper, and canteen full of water) and ensure that equipment is in good condition.  Prepare to direct students to decontaminate their eyes.  Direct the students to assume MOPP2, with the remaining MOPP gear available, to be evaluated on the procedures to decontaminate their eyes.

Note:	Do not use the decon wipes or decon powder on or in eyes.  Flush the eyes with water immediately if they come in contact with these.

Briefing:	You will decontaminate your eyes using the equipment provided.  You will be evaluated on your ability to demonstrate the steps necessary to decontaminate your eyes.  You must perform all steps correctly and sequentially to receive a GO on this task.

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

| NAME: |  | ELEMENT (SQUAD/SECTIONPLT/CO) |  | DATE: |
| --- | --- | --- | --- | --- |

| Performance Measures | Results |
| --- | --- |
| A. Decontaminate Eyes |  |  |
| 1. Dons the mask and hood without zipping the hood, pulling the draw strings, or fastening the shoulder straps. | GO | NO GO |
| 2. Removes canteen from LCE, and unscrews the cap. | GO | NO GO |
| 3. Checks canteen mouth for contamination using M8 Detector Paper. If canteen mouth is contaminated, obtains an uncontaminated canteen. CAUTION: Avoid possible contamination of canteen cap by pushing up on bottom of canteen cover until you can grasp the canteen by its body. | GO | NO GO |
| 4. Takes a deep breath and hold it. | GO | NO GO |
| 5. Unseals mask, lift it, and continues to hold breath. | GO | NO GO |
| 6. Flushes the eye(s) immediately with as much water as possible from canteen. | GO | NO GO |
| 7. To irrigate eyes with water from the canteen (or any other container of uncontaminated water): |  |  |
| a. Looks up and tilts head to the side to be decontaminated. | GO | NO GO |
| b. Opens eyes as wide as possible. | GO | NO GO |
| WARNING: Do not use fingers or gloved hand for holding the eyelids apart. This could cause further contamination. |  |  |
| c. Pours water slowly into the eye so that it will run off the side of face to avoid spreading contamination. | GO | NO GO |
| Note: Avoid letting the contaminated water run onto your clothing. |  |  |
| 8. Reseals, clears, and checks mask. Then resumes breathing. | GO | NO GO |

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

EVALUATION PREPARATION	(Decontaminate Skin Using the M258A1 Skin Decontamination Kit)

Setup:	Evaluate this objective within a field training environment.  Gather all necessary equipment (MOPP gear, a poncho, LCE, and the M258A1 Skin Decontamination Kit) and ensure that equipment is in good condition.  Ensure placement of the decontamination kit on the LCE or BDO of the individual or in the pocket of the mask carrier.  Prepare to direct students to decontaminate their skin.  Direct the students to assume MOPP2, with remaining MOPP gear available, to be evaluated on the procedures to decontaminate their skin.

Note:	For training and evaluation purposes, the M58A1 Training Aid Decontamination Kit will be substituted for the M258A1 Skin Decontamination Kit.  Do not use the decon wipes on or in eyes, mouth, or open wounds.  Flush these areas immediately with water if they come in contact with decon wipes.

Briefing:	You will decontaminate your skin using the M258A1 Skin Decontamination Kit.  You will be evaluated on your ability to demonstrate the steps necessary to decontaminate your skin.  You must perform all steps correctly and sequentially to receive a GO on this task.  You will decontaminate your face and hands during this test.

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

| NAME: |  | ELEMENT (SQUAD/SECTIONPLT/CO) |  | DATE: |
| --- | --- | --- | --- | --- |

| Performance Measures | Results |
| --- | --- |
| B. Decontaminate Skin with the M258A1 Skin Decontamination Kit |  |  |
| 1. Puts on protective mask and hood; seeks overhead shelter. | GO | NO GO |
| 2. Prepares the decon 1 wipe. |  |  |
| a. Opens decontamination kit. | GO | NO GO |
| b. Removes one decon 1 wipe packet by its tab. | GO | NO GO |
| c. Folds decon 1 wipe packet at the solid line marked BEND and then unfolds it. | GO | NO GO |
| d. Tears packet open quickly at notch, remove the wipe, and opens it fully. | GO | NO GO |
| 3. Wipes skin starting with hands. | GO | NO GO |
| NOTE: Ensure student holds breath while performing the steps to decontaminate the face. If student needs to breathe before he/she is finished, ensure he/she reseals the mask, clears it, checks it, and continues. |  |  |
| 4. Unseals mask as follows: |  |  |
| a. Holds breath. | GO | NO GO |
| b. Closes eyes. | GO | NO GO |
| c. Lifts hood and mask away from chin. | GO | NO GO |
| 5. Decontaminates face, if necessary. | GO | NO GO |
| NOTE: The corners of the mouth, areas of the nose and mouth, and chin are areas that are difficult to decontaminate. You should pay extra attention to these areas when wiping. |  |  |
| 6. Wipes up and down from ear to ear. |  |  |
| a. Starts at ear. | GO | NO GO |
| b. Wipes across face to the corner of nose. | GO | NO GO |
| c. Wipes an extra stroke at the corner of nose. | GO | NO GO |
| d. Wipes across nose and tip of nose to the corner of nose. | GO | NO GO |
| e. Wipes an extra stroke at the corner of nose. | GO | NO GO |
| f. Wipes across face to your other ear. | GO | NO GO |
| 7. Wipes up and down from ear to the end of jawbone. |  |  |
| a. Begins where step 6 ended. | GO | NO GO |
| b. Wipes across cheek to the corner of mouth. | GO | NO GO |
| c. Wipes an extra stroke at corner of mouth. | GO | NO GO |
| d. Wipes across closed mouth to the center of upper lip. | GO | NO GO |
| e. Wipes an extra stroke at center of upper lip. | GO | NO GO |
| f. Wipes across closed mouth to corner of mouth. | GO | NO GO |
| g. Wipes an extra stroke at corner of mouth. | GO | NO GO |
| h. Wipes across cheek to end of jawbone. | GO | NO GO |
| 8. Wipes up and down from one end of jawbone to other end of jawbone. |  |  |
| a. Begins where step 7 ended. | GO | NO GO |
| b. Wipes across and under jaw to chin, cupping your chin | GO | NO GO |
| c. Wipes an extra stroke at cleft of chin. | GO | NO GO |
| d. Wipe across and under jaw to end of jawbone. | GO | NO GO |
| 9. Turns hand out and quickly wipes the inside portions of the mask that touch face. | GO | NO GO |
| NOTE: Do not wipe mask lens. The decon solution will leave a film on the lens. |  |  |
| 10. Immediately seals, clears, and checks mask. | GO | NO GO |
| 11. Decontaminates neck and ears, if necessary, using the same decon 1 wipe. | GO | NO GO |
| 12. Drops wipe to the ground. | GO | NO GO |
| 13. Prepares decon 2 wipe. |  |  |
| a. Pulls one decon 2 wipe packet out of the case. | GO | NO GO |
| b. Crushes the enclosed glass ampoules between the thumb and fingers without kneading. | GO | NO GO |
| c. Folds the packet on the solid line marked CRUSH AND BEND. | GO | NO GO |
| d. Unfolds the packet. | GO | NO GO |
| e. Tears the packet open quickly at the notch. | GO | NO GO |
| f. Removes the wipe. | GO | NO GO |
| g. Opens the wipe fully. | GO | NO GO |
| h. Disposes of the crushed glass ampoule by letting it fall to the ground. | GO | NO GO |
| 14. Repeats steps 3 through 12 using the decon 2 wipe. | GO | NO GO |
| 15. Puts on protective gloves. | GO | NO GO |
| 16. Fastens hood. | GO | NO GO |
| 17. Makes sure all skin areas that have been decontaminated are covered. | GO | NO GO |

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

EVALUATION PREPARATION	(Decontaminate Individual Equipment Using the M258A1 Skin Decontamination Kit)

Setup:	Evaluate this objective within a field training environment.  Gather all necessary equipment (MOPP gear, a poncho, LCE, and the M258A1 Skin Decontamination Kit) and ensure that equipment is in good condition.  Ensure placement of the decontamination kit on the LCE or BDO of the individual or in the pocket of the mask carrier.  Prepare to direct students to decontaminate their skin.  Direct the students to assume MOPP2, with remaining MOPP gear available, to be evaluated on the procedures to decontaminate individual equipment.

Note:	For training and evaluation purposes, the M58A1 Training Aid Decontamination Kit will be substituted for the M258A1 Skin Decontamination Kit.  Do not use the decon wipes on or in eyes, mouth, or open wounds.  Flush these areas with water immediately if come in contact with decon wipes.

Briefing:	You will decontaminate your individual equipment using the M258A1 Skin Decontamination Kit.  You will be evaluated on your ability to demonstrate the steps necessary to decontaminate your individual equipment.  You must perform all steps correctly and sequentially to receive a GO on this task.  You will decontaminate your gloves, helmet, and mask for this test.

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

| NAME: |  | ELEMENT (SQUAD/SECTIONPLT/CO) |  | DATE: |
| --- | --- | --- | --- | --- |

| Performance Measures | Results |
| --- | --- |
| C. Decontaminate Individual Equipment the M258A1 Skin Decontamination Kit |  |  |
| NOTE: Do not use the decontaminating kit on protective overgarments. |  |  |
| 1. Decontaminates gloves and helmet using decon 1 wipe first, then decon 2 wipe. | GO | NO GO |
| 2. Decontaminates the exterior of the hood and mask. |  |  |
| a. Wipes eyelens outserts using a decon 2 wipe. | GO | NO GO |
| b. Begins wiping the hood at the top works downward. | GO | NO GO |
| c. Repeats these steps using a decon 1 wipe. | GO | NO GO |

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

EVALUATION PREPARATION	(Decontaminate Skin Using the M291 Skin Decontamination Kit)

Setup:	Evaluate this objective within a field training environment.  Gather all necessary equipment (MOPP gear, a poncho, LCE, and the M291 Skin Decontamination Kit) and ensure that equipment is in good condition.  Ensure placement of the decontamination kit on the LCE or BDO of the individual or in the pocket of the mask carrier.  Prepare to direct students to decontaminate their skin.  Direct the students to assume MOPP2, with remaining MOPP gear available, to be evaluated on the procedures to decontaminate their skin.

Note:	The M291 Skin Decontamination Kit should be used for both actual combat and for training purposes.  Do not use the decon powder on or in eyes, mouth, or open wounds. Flush these areas with water immediately if they come in contact with decon powder.

Briefing:	You will decontaminate your skin using the M291 Skin Decontamination Kit.  You will be evaluated on your ability to demonstrate the steps necessary to decontaminate your skin.  You must perform all steps correctly and sequentially to receive a GO on this task.  You will decontaminate your hands and face for this test.

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

| NAME: |  | ELEMENT (SQUAD/SECTIONPLT/CO) |  | DATE: |
| --- | --- | --- | --- | --- |

| Performance Measures | Results |
| --- | --- |
| D. Decontaminate Skin the M291 Skin Decontamination Kit |  |  |
| 1. Puts on protective mask and hood; seeks overhead cover. | GO | NO GO |
| 2. Removes one skin decon packet from the carrying pouch. | GO | NO GO |
| NOTE: Although any notch may be used to open the packet, opening at TEAR LINE will place the applicator in a position that is easier to use. |  |  |
| 3. Tears the packet open quickly at the notch. | GO | NO GO |
| 4. Removes the applicator pad from the packet. | GO | NO GO |
| 5. Discards the empty packet, observing litter discipline. | GO | NO GO |
| 6. Unfolds the applicator pad and slips finger(s) into the handle. | GO | NO GO |
| NOTE: For the following decontamination procedures, use the entire surface of the applicator pad. |  |  |
| 7. Scrubs the exposed skin of the back of the hand, palm, and fingers until completely covered with black powder from the applicator pad. | GO | NO GO |
| 8. Switches the applicator pad to the other hand and repeats step 7. | GO | NO GO |
| NOTE: Do not discard the applicator pad at this time. |  |  |
| 9. Starts the procedures to decontaminate the exposed skin of the face. At the completion of steps 10 through 16, the face will be completely covered with black powder from the applicator pad. | GO | NO GO |
| WARNING: Death or injury may result if you breathe toxic agents while decontaminating your face. If you need to breathe before you finish, reseal your mask, clear it, and check it. Get your breath, then resume the decontaminating procedure. |  |  |
| 10. Holds breath, closes eyes, grasps the mask beneath the chin, and pulls hood and mask away from chin enough to allow one hand between the mask and your face. Holds mask in this position during steps 11 through 15. | GO | NO GO |
| NOTE: The corners of the mouth, areas of the nose and mouth, and chin are areas that are difficult to decontaminate. You should pay extra attention to these areas when decontaminating. | GO | NO GO |
| 11. Scrubs up and down across face beginning at front of one ear to nose to other ear. |  |  |
| a. Scrubs across face to the corner of nose. | GO | NO GO |
| b. Scrubs an extra stroke at the corner of nose. | GO | NO GO |
| c. Scrubs across nose and tip of nose to the corner of nose. | GO | NO GO |
| d. Scrubs an extra stroke at the corner of nose. | GO | NO GO |
| e. Scrubs across face to other ear. | GO | NO GO |
| 12. Scrubs up and down across face beginning where step 11 ended, across the mouth, to the other end of jawbone. |  |  |
| a. Scrubs across cheek to the corner of mouth. | GO | NO GO |
| b. Scrubs an extra stroke at the corner of mouth. | GO | NO GO |
| c. Scrubs across closed mouth to the center of upper lip. | GO | NO GO |
| d. Scrubs an extra stroke at the center of upper lip. | GO | NO GO |
| e. Scrubs across closed mouth to the corner of mouth. | GO | NO GO |
| f. Scrubs an extra stroke at the corner of mouth. | GO | NO GO |
| g. Scrubs across cheek to the end of jawbone. | GO | NO GO |
| 13. Scrubs up and down across face beginning where step 12 ended, to the chin, and to the other end of jawbone. |  |  |
| a. Scrubs across and under jaw to chin, cupping chin. | GO | NO GO |
| b. Scrubs an extra stroke at the cleft of chin. | GO | NO GO |
| c. Scrubs across and under jaw to the end of jawbone. | GO | NO GO |

| 14. Turns hand out and quickly scrubs the inside portions of the mask that touch face. | GO | NO GO |
| --- | --- | --- |
| 15. Discards the applicator pad. | GO | NO GO |
| 16. Immediately seals, clears, and checks mask. Resumes breathing. | GO | NO GO |
| 17. Removes the second skin decon packet from the carrying pouch. | GO | NO GO |
| 18. Tears open the packet quickly at the notch. | GO | NO GO |
| 19. Removes the applicator pad from the packet and discards the empty packet. | GO | NO GO |
| 20. Unfolds the applicator pad and slip finger(s) into the handle. | GO | NO GO |
| NOTE: If you were already masked when you became contaminated and skipped steps 9 through 20, continue using the same applicator pad. |  |  |
| 21. Without breaking the seal between face and mask, thoroughly scrubs the skin of neck and ears until they are completely covered with black powder. | GO | NO GO |
| 22. Rewipes hands until completely covered with black powder. | GO | NO GO |
| 23. Discards applicator pad. | GO | NO GO |
| 24. Puts on protective gloves. | GO | NO GO |
| 25. Fastens hood. | GO | NO GO |
| 26. Removes the powder with soap and water when operational conditions permit. | GO | NO GO |

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

EVALUATION PREPARATION	(Decontaminate Individual Equipment Using The M295 Individual Equipment Decontamination Kit)

Setup:	Evaluate this objective within a field training environment.  Gather all necessary equipment (MOPP gear, a poncho, LCE, and the M295 Individual Equipment Decontamination Kit) and ensure that equipment is in good condition.  Ensure placement of the decontamination kit on the LCE or BDO of the individual or in the pocket of the mask carrier.  Prepare to direct students to decontaminate their individual equipment.  Direct the students to assume MOPP2, with remaining MOPP gear available, to be evaluated on the procedures to decontaminate their individual equipment.

Note:	The M295 Individual Equipment Decontamination Kit should be used for both actual combat and for training purposes.  Do not use the decon powder on or in eyes, mouth, or open wounds.  Flush these areas with water immediately if they come in contact with decon powder.

Briefing:	You will decontaminate your individual equipment using the M295 Individual Equipment Decontamination Kit.  You will be evaluated on your ability to demonstrate the steps necessary to decontaminate your individual equipment.  You must perform all steps correctly and sequentially to receive a GO on this task.  You will decontaminate your gloves, mask, and LCE for this test.

# DECONTAMINATE YOURSELF AND INDIVIDUAL EQUIPMENT USING CHEMICAL DECONTAMINATION KITS

# performance test

| NAME: |  | ELEMENT (SQUAD/SECTIONPLT/CO) |  | DATE: |
| --- | --- | --- | --- | --- |

| Performance Measures | Results |
| --- | --- |
| E. Decontaminate Individual Equipment Using the M295 Individual Equipment Decontamination Kit |  |  |
| 1. Removes one decon packet from the pouch. | GO | NO GO |
| 2. Tears the packet open quickly at any notch. | GO | NO GO |
| 3. Removes the decon mitt. | GO | NO GO |
| 4. Discards the empty packet. | GO | NO GO |
| 5. Unfolds decon mitt. | GO | NO GO |
| 6. Decontaminates protective glove. |  |  |
| a. Grasps green (non-pad) side of decon mitt with hand (not the hand used for writing). | GO | NO GO |
| b. Scrubs the other gloved hand with decon mitt to start the flow of decon powder onto glove. | GO | NO GO |
| c. Then rubs glove with decon mitt until completely covered with decon powder. | GO | NO GO |
| 7. Dons decon mitt. |  |  |
| a. Inserts decontaminated glove inside the decon mitt. | GO | NO GO |
| b. Makes sure the pad side is in the palm of the hand. | GO | NO GO |
| c. Makes sure thumb sticks through the appropriate thumbhole. | GO | NO GO |
| d. Tightens the wristband on the glove hand securely. | GO | NO GO |
| 8. Decontaminates the other protective glove by rubbing thoroughly with pad side of the decon mitt until it is covered with decon powder. | GO | NO GO |
| 9. Decontaminates individual equipment by rubbing with pad side of the decon mitt until thoroughly covered with decon powder. Pay special attention to areas which are hard to get into (for example, cracks, crevices, and absorbent materials). |  |  |
| a. Decontaminates the exposed areas of mask and hood. | GO | NO GO |
| b. Decontaminates weapon(s). | GO | NO GO |
| c. Decontaminates helmet by scrubbing it with decon mitt. | GO | NO GO |
| 10. Discards decon mitt. | GO | NO GO |
| 11. Removes another decon packet from the pouch. | GO | NO GO |
| 12. Tears the packet open quickly at any notch, removes the decon mitt, and discards the empty packet. | GO | NO GO |
| 13. Unfolds decon mitt. | GO | NO GO |
| 14. Decontaminates protective glove. | GO | NO GO |
| 15. Dons decon mitt. | GO | NO GO |
| 16. Finishes decontaminating individual equipment. |  |  |
| a. Decontaminates LCE and accessories (canteen, ammo pouch, first aid pouch, etc.) | GO | NO GO |
| b. Decontaminates mask carrying case. | GO | NO GO |
| c. Decontaminates protective boots. | GO | NO GO |
| d. Repeats the decon of protective gloves. | GO | NO GO |
| 17. If liquid contamination is still suspected or detected, gets another packet and repeat steps 1 through 7. Then rubs or blots areas where contamination is still suspected or detected. | GO | NO GO |
| 18. Discards decon mitt. | GO | NO GO |