DEPARTMENT OF THE ARMY

D COMPANY, 3RD BATTALION 509TH PIR

FORT RICHARDSON, ALASKA  99505-8400

APVR-ABNB-D-CO	           28 March 2006

MEMORANDUM FOR CSM Maggard, 4-25 BDE S-3 Plans NCO

SUBJECT:  After Action Review of Bulldog Trail Section Live Fire Exercise/Recovery SOP Recommendations

1.  From 14 March 2006 through 17 March 2006, D Company, 3-509 IN (ABN) conducted section live fires on Bulldog Trail using all organic direct fire weapon systems.  The purpose of this training was twofold: first, to sustain and further develop proficiency in mounted operations, and second, to confirm or deny the recovery plan provided in 4-25 BDE Mounted Warrior TACSOP.  The training balanced realism with safety and was beneficial to all who participated.  In an effort to improve training for ourselves and others, we have captured the following lessons learned:

a.  ISSUE: Over-reliance on “down” vehicle driver

DISCUSSION: As the TACSOP reads, the “down” vehicle’s driver is responsible for hooking up both vehicles.  If the vehicle is down, one would assume that the vehicle has been hit in some fashion.  If a vehicle is hit, then the occupants inside may or may not be capable of assisting in their own recovery.  Additionally, the occupants of a hit vehicle need to checked in order to begin triage procedures.

RECOMMENDATION:  Two soldiers, TC and loader (or driver) dismount the recovering vehicle.  One pulls security while the other does a quick check of the down vehicle and attaches the tow strap.  There is no reliance on the down vehicle to participate in its own recovery.  All this can happen faster than the current SOP.

b.  ISSUE:  Time wasted positioning vehicles/operating tow shackle screw

DISCUSSION:  The current SOP requires the down driver to be within arms reach of the tow strap located on the rear antennae of the recovering vehicle.  When the two vehicles are within arms reach, the down vehicle’s driver must reach both hands out of the vehicle to secure the recovering vehicles tow strap and then unscrew/screw the tow shackle screw, connecting both vehicles.    Once he is complete, the vehicle is ready to be recovered.

RECOMMENDATION:  Arrange the tow strap on the front bumper in such a way it is routed through the sling load loops on both bumpers and then routed against itself.  The excess can either be S-rolled against itself and secured with easily breakable material (quarter inch cotton webbing, zip ties, hook and pile tape, stuff sack, etc.)  The tow strap on the down vehicle is attached to the tow pintle on the recovering vehicle.  Once hook up is complete, they can complete their exfil.  Vehicle positioning is much easier when they do not have to get both vehicles within arms reach of the down vehicle’s driver.  On the back bumper, the tow strap is already secured in the tow pintel and the excess is either S-rolled, tucked into a stuff sack, or shut inside the back hatch.

c.  ISSUE: Tow straps made of flammable material

DISCUSSION:  In both the BDE and proposed SOP, we rely heavily on the use of nylon tow straps.  This only works if the down vehicle is not burning.  If the down vehicle is burning, then the tow straps strength will be significantly degraded, to the point that the tow straps will not endure the stress required for even a short exfil.

RECOMMMENDATION:  Tow straps and any SOP revolving around them are not all encompassing.  Any mounted element must be proficient with tow bars and they still need to be carried at the lowest level resources allow.  Additionally, some recovery situations require nothing short of securing the area and bringing in a wrecker.  Anyone using a “rapid” recovery technique must understand it’s very limited uses and that this SOP does not trump being situational aware and using common sense.  Additionally, have redundancy in our tow straps.  Each vehicle has a tow strap on the front and rear.  If the ones attached to the down vehicle are damaged, then they use the tow straps attached to the recovering vehicle.

e.  ISSUE: Posture

DISCUSSION:  Regardless of contact, any SOP that advises remaining in a vehicle does not promote an aggressive posture: we look like targets rather than killers.  Native populations, either in Afghanistan or Iraq, are very perceptive to our actions.  Remaining behind our armor could be easily misconstrued as being afraid of the native population, especially following contact.

RECOMMENDATION:  Dismount the vehicle, always maintain security, and don’t look like a target.  Have an aggressive attitude and the posture of a killer.

f. 	ISSUE: Location of secured tow straps

DISCUSSION: The front tow strap is secured on a side mirror, a piece of equipment that is normally removed or broken off.  The rear tow strap is secured on the rear, right antennae.  Both have the loops exposed and will create a huge shock to the crew of the vehicle that catches a loop on an obstruction on a narrow road or oncoming traffic.

RECOMMENDATION:  Keep the exposed loops of the tow straps center mass on the vehicles to prevent catching them on obstacles.

g.  ISSUE: Implied use of Recovery SOP during contact

DISCUSSION:  The only reason it makes sense to remain in a vehicle during recovery is if you are engaged in contact.  Otherwise you are just making a simple process very difficult.

RECOMMENDATION:  If at all possible, destroy the contact and then recover any down assets.  Recovery is a consolidation and reorganization task that must be accomplished extremely quickly, not a battle drill.

2.  If there are any questions, please contact me at (907) 384-1111 or by email at NAME@us.army.mil.

//--original signed--//

NAME

CPT, IN

Commanding