Shipping Instructions for

CHEMICAL AGENT MONITOR, NSN: 6665-01-199-4153

IMPROVED CHEMICAL AGENT MONITOR, NSN: 6665-01-357-8502

Isotope and Activity: Ni-63, 3.7E+08 Bq (10 mCi).

Basic Description: Radioactive material, excepted package - instruments or articles, 7, UN2911.

Chemical and/or Physical Form: Plated Ni-63, solid, normal form.

Package Requirements:

Packaging: Excepted Packaging.

Package Label: Exempt.

Package Marking: Exempt. Container must be marked in a visible location “Radioactive Material, UN2911”.

Survey Requirements:

Radiation Survey: Required prior to shipment.

- The radiation level at 10 cm (4 inches) from any point on the external surface of any unpackaged instrument or article shall not exceed 0.1 mSv/hr (10 mrem/hr). The radiation level at any point on the external surface of the package shall not exceed 0.005 mSv/hr (0.5 mrem/hr).

- Contamination Wipe Survey: No annual wipe test required for the CAM or ICAM unless unit is damaged.  Only required prior to shipment on reused containers, new containers do not require a wipe test. The non-fixed radioactive contamination on the external surfaces of the package shall not exceed 22 dpm/cm2 (beta).

Transportation Requirements:  Declared shipments are permitted aboard passenger-carrying aircraft, per 49 CFR 173.422. Forms to be used:

- Military Airlift – Army Radioactive Movement Form or Movement Memorandum

- Commercial Air – Shipper’s Declaration for Dangerous Goods (Red Border)

Vehicle Placarding: Not required.

Additional Requirements: You shall certify this radioactive material for transportation by having a notice enclosed in or on the package, included with the packing list, or otherwise forwarded with the package. This notice must include the name of the consignor or consignee, Serial Number inventory and the statement signed by a certified hazardous material transportation representative:

I Certify “THIS PACKAGE CONFORMS TO CONDITIONS AND LIMITATIONS SPECIFIED IN 49 CFR 173.424 FOR RADIOACTIVE MATERIAL, EXEPTED PACKAGE FOR ARTICLES AND INSTRUMENTS, Per Table 7, UN2911 Applies”

Additional Comments:

- Military Radiation Movement Form is required w/serial inventory inside the package

- There is a maximum of 3.0 E+13 Bq (810.8 Ci) total activity for Ni-63 that you may ship per package.

- You may mail (USPS) up to 3.0 E+12 Bq (81.08 Ci) total activity of Ni-63 per package; all other 49 CFR conditions applicable to excepted packages for radioactive instruments and articles apply.

- Equipment cannot be in the same Container as Explosive and/or Flammable material and must be placed so that it is the first item removed from the container.