## Slide 1
High Mobility Multipurpose Wheeled Vehicle (HMMWV)
Egress Assistance Trainer
HEAT
Notes: <number>

## Slide 2
Terminal Learning Objective
Action: | Perform clearing, and egress procedures with the HEAT.
Conditions: | In the HEAT wearing required combat equipment , given instruction on actions to take to preclude and reactive measures during/after a HMMWV rollover as a HMMWV crewmember.
Standards: | Properly evacuate the HEAT while adhering to applicable safety precautions and procedures outlined in this lesson and applicable references.
Notes: <number>

## Slide 3
Rollover battle drills create an understanding of and how to react to the violent chaos that results when a rollover has occurred.
ACTION: | Understand preventive measures to preclude rollover
CONDITIONS: | In a classroom, provided instruction on preventive and reactive measures, crewman duties and emergency steps to take to preclude a vehicle rollover.
STANDARDS: | Identify precautionary measures to take to prevent a HMMWV vehicle rollover by answering the check-on-learning questions posed by instructor with a minimum of 80%.
ENABLING LEARNING OBJECTIVE A:
Notes: <number>

## Slide 4
Combat Patrol-loaded M1114
less than 30°
Critical Rollover Angle
Current Version of Up-armored HMMWV
25° *
* less with higher-cg loads
25°
30°
Notes: <number>

## Slide 5
Rollovers are caused by
Speed
Inadequate training
High centers of gravity
Terrain
Road conditions,
Driving habits
Local conditions
Causes of Rollovers
Notes: <number>

## Slide 6
Driver Risk Management Control Measures
Adjust the vehicle speed
Slow down
Avoid panic
Observe speed limit
Do not rely on a "seat of the pants"
Slowly accelerate
Maintain a "space cushion"
Avoid the temptation to brake hard
Notes: <number>

## Slide 7
Teamwork is Key
• Work as a team
• Maintain crew integrity
• Communicate with the driver
• Identify terrain or conditions favorable for a rollover
• Use a guide near bodies of water
• Position team members within the vehicle
Combat Locks
Know how to get out
Notes: <number>

## Slide 8
Price of Uparmored HMMWVs
Extremely-top heavy
Vehicle rollovers common and deadly occurrence
Notes: <number>

## Slide 9
Steps When Rollover Anticipated Not Into Water
Driver:
(1) Releases the accelerator.
(2) Shouts, "Rollover, Rollover, Rollover!"
(3) Keeps hands on the steering wheel with arms extended but not locked.
(4) Plants feet firmly on the floor.
(5) Tucks head and chin into chest and braces for impact.
Vehicle Commander (VC):
(1)Shouts, "Rollover, Rollover, Rollover!"
(2) Uses left hand to pull gunner into the vehicle.
(3) Uses left hand and arm to hold the gunner in place.
(4) Plants feet firmly on the floor while holding onto a stationary object.
(5) Tucks head and chin into chest and braces for an impact.
Notes: <number>

## Slide 10
Steps When Rollover Anticipated Not Into Water
Gunner:
(1) Shouts, "Rollover, Rollover, Rollover!"
(2) Pushes/pulls self down into the vehicle.
(3) Holds onto a stationary object.
(4) Tucks head and chin into chest and braces for impact.
(5) Does not place hands or fingers on turret
Other Crewmembers:
(1) Shout, “Rollover, Rollover, Rollover!"
(2) Assist VC to pull gunner into the vehicle and hold him.
(3) Tuck heads and chins into chests and brace for impact.
(4) Hold onto a stationary object.
Notes: <number>

## Slide 11
Water Entry Is Imminent
Whether Or Not The Potential For A Rollover Exists
VC: (When in the vicinity of water and tactical conditions permit)
(1) Informs vehicle crew that the vehicle is operating around water hazards.
(2) Reminds the crew of the risk mitigating measures.
(3) Unlocks the combat door locks.
(4) Ensures all loose gear and cargo are secured.
Driver:
Releases the accelerator; controls entry by steering into the body of water
(2) Yells "Water!"
(3) Keeps hands on the steering wheel with arms extended but not locked.
(4) Plants feet firmly on the floor.
(5) Tucks head and chin into chest and braces for impact.
Notes: <number>

## Slide 12
Water Entry Is Imminent
Whether Or Not The Potential For A Rollover Exists
VC:
(1) Shouts, "Water!"
(2) Uses left hand to pull gunner into the vehicle.
(3) Uses left hand and arm to hold the gunner in place.
(4) Plants feet firmly on the floor while holding onto a stationary object.
(5) Tucks head and chin into chest and braces for an impact.
Other crewmembers (if present):
(1) Shout, "Water!"
(2) Assist VC to pull gunner into the vehicle and hold him.
(3) Tuck head and chin into chest and brace for impact.
(4) Plant feet firmly on floor while holding onto a stationary object.
Gunner:
(1) Yells, "Water!"
(2) Pushes/pulls self down into the vehicle.
(3) Slides feet in the direction of the vehicle's movement.
(4) Plants feet firmly on the floor while holding onto a stationary object.
(5) Tucks head and chin into chest and braces for impact.
(6) Does not place hands or fingers on turret.
Notes: <number>

## Slide 13
ENABLING LEARNING OBJECTIVE B:
ACTION: | Understand measures to take after rollover
CONDITIONS: | In a classroom, provided instruction on reactive measures, crewman duties and emergency steps to take in case of a vehicle rollover
STANDARDS: | Identify reactive measures to take in case of a HMMWV vehicle rollover by answering the check-on-learning questions posed by instructor with a minimum of 80%.
Notes: <number>

## Slide 14
After Rollover (Not In Water)
Each crewmember, whether driver, VC, or rear crew:
(1) Braces one hand on the ceiling.
(2) Unbuckles seatbelt with other hand and immediately puts both hands on ceiling.
(3) Slides out of seat and sits up.
(4) Disconnects headset.
(5) Turns off motor (driver).
(6) Orients self on the nearest door.
(7) Unlocks combat door locks.
(8) Opens door; if it does not open, try a different door. (Shouts Door to notify other soldiers of open door allowing egress)
(9) Exits with weapon.
(10) Assists remaining crew to exit.
(11) Establishes security.
(12) Checks for fires.
(13) Activates fire extinguisher, as needed.
(14) Recovers sensitive items.
(15) Provides first aid.
(16) Assists in vehicle recovery.
Notes: <number>

## Slide 15
After Rollover (Not In Water)
Gunner:
(1) Disconnects headset.
(2) Releases Gunners Restraint System/Product Improved Gunner’s Restraint System
(3) Orients self on the nearest door.
(4) Unlocks combat door locks.
(5) Opens door; if it does not open, tries a different door.
(6) Exits with weapon.
(7) Assists crew to exit.
(8) Establishes security.
(9) Checks for fires.
(10) Activates fire extinguisher, as needed.
(11) Recovers sensitive items.
(12) Provides first aid.
(13) Assists in vehicle recovery.
Notes: <number>

## Slide 16
If Vehicle Rolls Onto Side
Lower level Soldiers, if able:
(1) Unbuckle seat belts.
(2) Assist upper Soldiers to unfasten seat belts then carefully lower.
Crew, if doors are jammed:
(1) Exit through hatch or cargo area if possible.
(2) Work as a team to open jammed doors.
Notes: <number>

## Slide 17
After Rollover (In Water)
All crewmembers:
(1) Turn off motor (driver).
(2) Disconnect headsets.
(3) Unbuckle seatbelt with other hand and immediately put both hands on ceiling.
(4) Unlock combat door locks if not already unlocked.
(5) Decide whether or not to remove personal equipment.
(6) Exit the vehicle.
(7) Assist each other to exit and secure weapons.
(8) Assess injuries.
(9) Get to safest shore.
(10) Provide security.
(11) Account for other crewmembers.
(12) Provide/seek first aid.
(13) Retrieve weapons, ammunition, and sensitive items.
(14) Assist with vehicle recovery.
VC:
(1) Accounts for weapons, ammunition, and sensitive items
(2) Requests medical support, if required.
(3) Reports accident.
Notes: <number>

## Slide 18
Water Rescue Recovery Drill
a. Rescuers secure the accident site.
b. Stay in contact with the vehicle.
c. Rescuers tie a rope/cable to the vehicle
to aid rescue.
d. Open doors and hatches.
e. Turn vehicle if doors and hatches
are not accessible.
f. Seek out the highest point on vehicle.
g. Ensure all survivors have air.
h. Check for other injuries and apply first aid.
i. Remove personal equipment.
j. Move injured personnel to the highest point on the vehicle.
k. Evacuate safest location, depending on:
(1) Enemy situation
(2) Water level and flow
(3) Water temperature
(4) Distance to water's edge
(5) Anticipation of rescue
Notes: <number>

## Slide 19
Check On Learning
1. A combat patrol loaded M1114, with a normal center of gravity (cg) and normal load can operate on slopes of up to:
a. 20 degrees.
b. 25 degrees.
c. 30 degrees.
d. 98.6 degrees.
2. The critical (rollover) angle for current version in theater up-armored HMMWV is:
a. 20 degrees.
b. 25 degrees.
c. 30 degrees.
d. 98.6 degrees.
3. The corrective action before reaching the critical rollover angle is:
a. Jerk the wheel back to the center of the road.
b. All occupants yell, “Water!”
c. Gradually reduce speed and ease the vehicle back onto the roadway at a safe speed.
d. Secure the coolers and secure voice radios.
4. During egress, you find the door you’re attempting to exit won’t open. You should:
a. Inflate your water wings, kick out the windshield, and swim away from the enemy.
b. Don’t panic - find a door that works.
c. Stay put and call the Auto club.
d. Stay put and call QRF on the secure voice radio.
Notes: <number>

## Slide 20
Check On Learning
5. What are the egress actions for the Gunner following a rollover on dry land?
a. Disconnect headset, release gunner’s restraint system, assess injuries, clear and check weapon, exit vehicle with weapon.
b. Assist crew to exit, establish security, recover sensitive items, provide first aid and assist in vehicle recovery.
c. a and b above.
d. Leap from the vehicle before it rolls.
6. What are the immediate actions of the Driver should an entry into the water be imminent?
a. Release the accelerator; yell “Water!” and keep hands on the steering wheel.
b. Tuck head and chin into chest and brace for impact; and steer vehicle to control entry into the water to prevent rollover.
c. a and b above.
d. Leap from the vehicle before it hits the water.
7. Prior to releasing your seatbelt for egress, and immediately afterward, you must:
a. Brace with one hand against what was the ceiling (consider which hand you should brace with) – your neck cannot support your body weight during a fall; unfasten your seatbelt with the other hand.
b. Unfasten your seatbelt with one hand, pushing firmly until it pops loose. You may have to push against the floor with your bracing hand to allow the seatbelt to unfasten.
c. a and b above.
d.Take out your k-bar and cut the thing off.
Notes: <number>

## Slide 21
Check On Learning
8. What is the purpose of the combat door lock?
a. To prevent aggressors from entering the vehicle in a hostile area.
b. It interfaces with the Lojack circuitry, and assists police in recovery of a stolen HMMWV.
c. It jettisons the door if moisture is detected during a water entry.
d. There is no difference between a combat door lock and a conventional door lock.
9. When operating near bodies of water or crossing bridges, the HMMWV crew should:
a. Inform crewmembers of the water hazard, loosen seatbelts, slow down.
b. Identify water hazards, unlock combat locks, remove seatbelts, slow down.
c. Slow down, inform crewmembers of possible water hazards, unlock combat locks (enemy situation permitting).
d. Look for alternate routes.
10. To reduce the risk of being involved in a rollover, HMMWV crews should:
a. Check tires for proper inflation and serviceability, and slow down.
b. Slow down, don’t overload the vehicle, check condition and serviceability of tires, secure loads.
c. Ensure operators are properly licensed.
d. Limit crews operating in the vehicle to four or less.
Notes: <number>

## Slide 22
Check On Learning
11. What can gunners do to minimize their injuries when involved in a rollover?
a. Try to jump away from the vehicle.
b. Lower yourself and brace for impact.
c. Yell “Rollover!” while lowering yourself into the vehicle, bracing for impact.
d. Call the Automobile Club and complain about that last sharp curve in the road.
12. What preventive measures can be taken to minimize the chances of being involved in a rollover?
a. Make a detailed Power Point presentation of any sharp curve in the road for emailing to your Congressman in a formal yet anonymous complaint.
b. License and certify all crews on the HEAT, and train as a team.
c. Slow down, avoid panic, know proper vehicle maneuvering, use caution in rural areas with soft shoulders, and identify water hazards.
d. None of the above – only tracking your number of days left in country will help.
13. Other than the driver and gunner, what are the duties of the crew in the event of a rollover?
a. Yell “Rollover!”
b. Grab the gunner and pull them into the crew compartment.
c. Brace for impact.
d. All of the above.
Notes: <number>

## Slide 23
ENABLING LEARNING OBJECTIVE C:
Practical Exercise
ACTION: | HEAT operator performance drill familiarization
CONDITIONS: | In the HEAT trainer with required equipment and previous training.
STANDARDS: | Properly evacuate the HEAT while and adhering to applicable safety precautions and procedures outlined in this lesson and applicable references.
Crew/Battle Drill Descriptions
1. The first drill is for familiarization, pausing to highlight the 30- and 25-degree critical rollover angles and righting the device back. 2. The second drill shall be a “dry run” – completely rolling over (inverted) – no actual release of the seatbelts or gunner’s harness will be made. 3. The third will entail inverting the device, and participants actually exiting the device, as though it had rolled on dry land. 4. After righting the device, crew rotating seats and re-entering the device – the fourth drill will entail inverting the device, simulating a water entry.
Notes: <number>

## Slide 24
ENABLING LEARNING OBJECTIVE C:
Practical Exercise
Notes: <number>