## Slide 1: TEMPORARY HULL REPAIR

## Slide 4: DAMAGE CONTROL (DC) TEAM
Chief Engineer
Assistant engineer
Boatswain
Seaman
Engineman

## Slide 5: PRELIMINARY WORK
90% of all DC work should be accomplished prior to ever getting underway.

## Slide 6: SIGNALS FOR DC EMERGENCIES

## Slide 7: Fire and Emergencies
Rapid ringing of the ship’s bell, and a continuous sounding of the general alarm for a period of at least 10 seconds.

## Slide 8: ABANDON SHIP
More than 6 short blasts and one long blast on the whistle and the same signal on the general alarm.

## Slide 9: MAN OVERBOARD
Hail and pass the word to the bridge. ( Hail means to shout )
Indicate which side the person fell overboard. Point to the person to help the bridge locate the person. ( mark the spot )

## Slide 10: Secure from drill
Three short blasts accompanied by three rings of the general alarm.

## Slide 11: DRILLS
Held Weekly.
Most vessels don’t practice damage control.

## Slide 12: COMPARTMENTATION ABOARD SHIP

## Slide 13: HORIZONTAL DIVISION
Decks are numbered from the main deck both upward and downward.
Below the main deck the numbers will increase. i.e. 1,2,3...
Above the main deck, the numbers will also increase, but will have a zero preceding it. i.e. 01,02,03...

## Slide 14: VERTICAL DIVISION
USES BULKHEADS TO MARK VERTICAL BOUNDARIES.
Vertical and horizontal division make up compartments.

## Slide 15: NUMBERING SYSTEM
First two numbers indicate which deck.
Second two numbers indicate the frame number where the compartment starts ( usually the forwardmost frame ).
single or double numbers indicate the compartments relation to the centerline.
Single or double letter indicate the use of the compartment.

## Slide 16
comp. use list ( partial list )
A-Storeroom
AA-Cargo storeroom
C-Ship control
E-Engineering space
F-Fuel
L-Living space
V-Void
W-Water ( tanks )

## Slide 17
Compartment 01-46-0-C
Located on the 01 deck ( one deck above the main deck )
starting at frame 46
used for ship control

## Slide 19: MATERIAL CONDITIONS OF READINESS
Condition XRay- Black “X” on white or metallic background. will be on the fitting to be closed or close to the fitting.
  Closed at all times unless actually in use. This condition is set at all times aboard ship. It is the lowest most relaxed setting aboard.
  Can be modified.

## Slide 21
Condition yoke- Black “y” on white or metallic background. Will be on or close to the fitting.
Will be set at sea in peacetime. It is also set when entering or leaving port.

## Slide 22
During wartime it will be set while in port. this provides the second step in setting the basic battle condition.
this condition may be modified to meet existing conditions.

## Slide 23
Condition Zebra- This is a red Z on a metallic or white background.
This is the third step or battle condition, this will be set for fire, collision. General emergency and entering or leaving port in wartime

## Slide 24
Do not open an x,y or z fitting without permission from the proper authority
Certain fittings may be modified. These fittings will have a circle around the x,y,z. This means you may open the fitting to pass and then close it after you.

## Slide 25: Scope of Damage control
Damage control covers both battle and non battle damage caused by.
  Fire
  Collision
  Grounding
  Explosions
  Loading incorrectly or to heavy a load.

## Slide 26: OBJECTIVES OF DAMAGE CONTROL
Prevention
  Preserve watertight integrity before getting underway.
Control of damage
  Set up flood boundaries if damage occurs.
Repairs
  Speed is essential
Training

## Slide 27: BREAK TIME
Take Ten

## Slide 28: DC COURSES OF ACTION
Plug and patch holes.
establish and maintain flood boundaries.

## Slide 29: FACTORS AFFECTING UNDERWATER REPAIR
Pressure exerted by the sea (approximately 3 psi ).
Relative inaccessibility of the damage.

## Slide 30: PLUGGING AND PATCHING MATERIAL
Wooden plugs
Wooden wedges
Prefabricated box patches (wood and steel )
Collapsible hinge plates

## Slide 31: SECURING MATERIALS
Eye bolts
Chain hoists/ come-a-longs
Hook bolts
Manila line
Angle clips
Shoring
Nails

## Slide 32: GASKET MATERIALS
Sheet and strip rubber
Leather/ canvas
Rags
Oakum
Stuffing compound

## Slide 33: PLUGGING
Unless a hole is perfectly round ( which is extremely rare ), it is best to use a combination of conical square ended and wedged shaped plugs.

## Slide 35: PATCHES

## Slide 36: FOLDING PLATE PATCH
Same as plate patch except the metal is lighter and more flexible.
it is used to seal curved sides of the vessel.

## Slide 37: PLATE PATCH
Made from a length of steel plate.
usually spot welded to the sides of the vessel.

## Slide 38: COLLAPSIBLE HINGE PLATE
Used on holes up to 18” in diameter.
Patches can be made of an ordinary piece of plywood or from metal.

## Slide 39: COLLISION MAT
Large canvas mats covered on one side with long hairlike fibers.
Carried over the outsides of holes and held in place with various guys.

## Slide 40: BOX PATCHING
Effective over holes that have jagged edges protruding inboard.

## Slide 41: PIPE PATCHING
Damaged pipes are another cause of flooded compartments.
You may isolate the leak by securing the valve.
For small holes, drill out and insert a machine screw.

## Slide 42: Jubilee patch
Uses a prefabricated cylinder of metal with flanges and holes in pipe. Wing nuts are provided to anchor the patch. Gasket material may be used.

## Slide 43: Soft patch
Uses a soft wood plug or a wedge to drive in the split, cut it off, then use gasket material to seal the area off. You may then wrap the outside with either marline, or other suitable material.

## Slide 44: CRACKS
Prevention
  Keep cracks from spreading by drilling a 1/4 inch hole at each end of the crack.

## Slide 45: BREAK TIME

## Slide 46: SHORING
Shoring is used to support ruptured decks, strengthen weakened bulkheads, hold patches in place or detached equipment.

## Slide 48: EFFECTIVE SHORING
Clear the decks of wreckage.
Speed
Preparation

## Slide 49: SHORES
A shore is a portable beam that has not been painted. The shore is made of soft wood, such as yellow pine, Douglas fir, hemlock or spruce.
Shores usually are received on board in 20ft. lengths.

## Slide 50: SHORES
The length of a shore should never be more than thirty times its minim thickness.
I.E.. 4X4 Shore 4x30=120/12=10ft.

## Slide 51: WEDGES
Should be of a soft wood that is coarse cut and left unpainted.
Wedges should be the same width, or larger than, the shore they are serving.
Wedges should be 5 to 6 times the height of the butt.

## Slide 52
They should always be used in pairs.
If wedges need to be secured use a cleat.

## Slide 53: SHOLES
Should be made of Douglas fir or yellow pine that is at least 1” thick and 8” to 12” wide.
Sholes are used to distribute pressure and/or prevent shores from splitting on rivets or seams.

## Slide 54: STRONGBACKS
All or part of a shore may be used to make a strongback.
A strong back distributes pressure across a patch or shole.

## Slide 55: STRONGBACK

## Slide 56: TOOLS USED FOR SHORING
Sledge hammer
Crosscut saw
10’ and 50’ metal tape rule
Lumber crayon
Hatchet
Emergency light source
2 lbs of nails( 20d & 30 d )

## Slide 57: TOOLS
Carpenter square
Shoring batten
Chain saw

## Slide 58: SHORING STRUCTURES
Direct Compression - Strongest, easiest, and quickest structure to erect.
Triangular/Triangulation - Second best structure takes time to build. make sure the legs of the shoring are set between 45 and 90 degrees.

## Slide 60: BREAK TIME

## Slide 61: DEWATERING MEASURES

## Slide 62: LOOSE WATER
Water with a free surface.

## Slide 63: SOLID WATER
flooded compartment

## Slide 64: NOTE
Compartments must be dewatered in a manner that will contribute to the overall stability of the ship.

## Slide 65: DEWATERING PUMPS
Fixed bilge pump
P-250 portable pump

## Slide 66: FIXED BILGE PUMPS
Will pump water directly overboard

## Slide 67: P-250 PORTABLE PUMP
Has A 250 gpm rating.
Self priming lift of 16 - 20 ft.
Two stroke/ two cycle engine.
5oz of oil per gallon of gas.
Do not run more than 45 seconds without pressure on the gauge.

## Slide 68: PMCS
Performed by engineers.
Run 10-15 min. weekly during emergency drills.
Keep tank full to prevent condensation.
Boatswain ensures task is completed.

## Slide 69: DAMAGE CONTROL