## Slide 1
Phase III VG 1

## Slide 2
Phase III VG 2

## Slide 3
Phase III VG 3

## Slide 4: DAMAGE CONTROL (DC) TEAM
Chief Engineer
Assistant engineer
Boatswain
Seaman
Engineman
Phase III VG 4

## Slide 5: PRELIMINARY WORK
90% of all DC work should be accomplished prior to ever getting underway.
Phase III VG 5

## Slide 6: SIGNALS FOR DC EMERGENCIES
Phase III VG 6

## Slide 7: Fire and Emergencies
Rapid ringing of the ship’s bell, and a continuous sounding of the general alarm for a period of at least 10 seconds.
Phase III VG 7

## Slide 8: ABANDON SHIP
More than 6 short blasts and one long blast on the whistle and the same signal on the general alarm.
Phase III VG 8

## Slide 9: MAN OVERBOARD
Hail and pass the word to the bridge. ( Hail means to shout )
Indicate which side the person fell overboard. Point to the person to help the bridge locate the person. ( mark the spot )
Phase III VG 9

## Slide 10: Secure from drill
Three short blasts accompanied by three rings of the general alarm.
Phase III VG 10

## Slide 11: DRILLS
Held Weekly.
Most vessels don’t practice damage control.
Phase III VG 11

## Slide 12: COMPARTMENTATION ABOARD SHIP
Phase III VG 12

## Slide 13: HORIZONTAL DIVISION
Decks are numbered from the main deck both upward and downward.
Below the main deck the numbers will increase. i.e. 1,2,3...
Above the main deck, the numbers will also increase, but will have a zero preceding it. i.e. 01,02,03...
Phase III VG 13

## Slide 14: VERTICAL DIVISION
USES BULKHEADS TO MARK VERTICAL BOUNDARIES.
Vertical and horizontal division make up compartments.
Phase III VG 14

## Slide 15: NUMBERING SYSTEM
First two numbers indicate which deck.
Second two numbers indicate the frame number where the compartment starts ( usually the forwardmost frame ).
single or double numbers indicate the compartments relation to the centerline.
Single or double letter indicate the use of the compartment.
Phase III VG 15

## Slide 16
comp. use list ( partial list )
A-Storeroom
AA-Cargo storeroom
C-Ship control
E-Engineering space
F-Fuel
L-Living space
V-Void
W-Water ( tanks )
Phase III VG 16

## Slide 17
Compartment 01-46-0-C
Located on the 01 deck ( one deck above the main deck )
starting at frame 46
used for ship control
Phase III VG 17

## Slide 18: MATERIAL CONDITIONS OF READINESS
Condition XRay- Black “X” on white or metallic background. will be on the fitting to be closed or close to the fitting.
  Closed at all times unless actually in use. This condition is set at all times aboard ship. It is the lowest most relaxed setting aboard.
  Can be modified.
Phase III VG 18

## Slide 19
Phase III VG 19

## Slide 20
Condition yoke- Black “y” on white or metallic background. Will be on or close to the fitting.
Will be set at sea in peacetime. It is also set when entering or leaving port.
Phase III VG 20

## Slide 21
During wartime it will be set while in port. this provides the second step in setting the basic battle condition.
this condition may be modified to meet existing conditions.
Phase III VG 21

## Slide 22
Condition Zebra- This is a red Z on a metallic or white background.
This is the third step or battle condition, this will be set for fire, collision. General emergency and entering or leaving port in wartime
Phase III VG 22

## Slide 23
Do not open an x,y or z fitting without permission from the proper authority
Certain fittings may be modified. These fittings will have a circle around the x,y,z. This means you may open the fitting to pass and then close it after you.
Phase III VG 23

## Slide 24: Scope of Damage control
Damage control covers both battle and non battle damage caused by.
  Fire
  Collision
  Grounding
  Explosions
  Loading incorrectly or to heavy a load.
Phase III VG 24

## Slide 25: OBJECTIVES OF DAMAGE CONTROL
Prevention
  Preserve watertight integrity before getting underway.
Control of damage
  Set up flood boundaries if damage occurs.
Repairs
  Speed is essential
Training
Phase III VG 25

## Slide 26: BREAK TIME
Take Ten
Phase III VG 26

## Slide 27: DC COURSES OF ACTION
Plug and patch holes.
establish and maintain flood boundaries.
Phase III VG 27

## Slide 28: FACTORS AFFECTING UNDERWATER REPAIR
Pressure exerted by the sea (approximately 3 psi ).
Relative inaccessibility of the damage.
Phase III VG 28

## Slide 29: PLUGGING AND PATCHING MATERIAL
Wooden plugs
Wooden wedges
Prefabricated box patches (wood and steel )
Collapsible hinge plates
Phase III VG 29

## Slide 30: SECURING MATERIALS
Eye bolts
Chain hoists/ come-a-longs
Hook bolts
Manila line
Angle clips
Shoring
Nails
Phase III VG 30

## Slide 31: GASKET MATERIALS
Sheet and strip rubber
Leather/ canvas
Rags
Oakum
Stuffing compound
Phase III VG 31

## Slide 32: PLUGGING
Unless a hole is perfectly round ( which is extremely rare ), it is best to use a combination of conical square ended and wedged shaped plugs.
Phase III VG 32

## Slide 33
Phase III VG 33

## Slide 34: FOLDING PLATE PATCH
Same as plate patch except the metal is lighter and more flexible.
it is used to seal curved sides of the vessel.
Phase III VG 34

## Slide 35: PLATE PATCH
Made from a length of steel plate.
usually spot welded to the sides of the vessel.
Phase III VG 35

## Slide 36: COLLAPSIBLE HINGE PLATE
Used on holes up to 18” in diameter.
Patches can be made of an ordinary piece of plywood or from metal.
Phase III VG 36

## Slide 37: COLLISION MAT
Large canvas mats covered on one side with long hairlike fibers.
Carried over the outsides of holes and held in place with various guys.
Phase III VG 37

## Slide 38: BOX PATCHING
Effective over holes that have jagged edges protruding inboard.
Phase III VG 38

## Slide 39: PIPE PATCHING
Damaged pipes are another cause of flooded compartments.
You may isolate the leak by securing the valve.
For small holes, drill out and insert a machine screw.
Phase III VG 39

## Slide 40: Jubilee patch
Uses a prefabricated cylinder of metal with flanges and holes in pipe. Wing nuts are provided to anchor the patch. Gasket material may be used.
Phase III VG 40

## Slide 41: Soft patch
Uses a soft wood plug or a wedge to drive in the split, cut it off, then use gasket material to seal the area off. You may then wrap the outside with either marline, or other suitable material.
Phase III VG 41

## Slide 42: CRACKS
Prevention
  Keep cracks from spreading by drilling a 1/4 inch hole at each end of the crack.
Phase III VG 42

## Slide 43: BREAK TIME
Phase III VG 43

## Slide 44: SHORING
Shoring is used to support ruptured decks, strengthen weakened bulkheads, hold patches in place or detached equipment.
Phase III VG 44

## Slide 45
Phase III VG 45

## Slide 46: EFFECTIVE SHORING
Clear the decks of wreckage.
Speed
Preparation
Phase III VG 46

## Slide 47: SHORES
A shore is a portable beam that has not been painted. The shore is made of soft wood, such as yellow pine, Douglas fir, hemlock or spruce.
Shores usually are received on board in 20ft. lengths.
Phase III VG 47

## Slide 48: SHORES
The length of a shore should never be more than thirty times its minim thickness.
I.E.. 4X4 Shore 4x30=120/12=10ft.
Phase III VG 48

## Slide 49: WEDGES
Should be of a soft wood that is coarse cut and left unpainted.
Wedges should be the same width, or larger than, the shore they are serving.
Wedges should be 5 to 6 times the height of the butt.
Phase III VG 49

## Slide 50
They should always be used in pairs.
If wedges need to be secured use a cleat.
Phase III VG 50

## Slide 51: SHOLES
Should be made of Douglas fir or yellow pine that is at least 1” thick and 8” to 12” wide.
Sholes are used to distribute pressure and/or prevent shores from splitting on rivets or seams.
Phase III VG 51

## Slide 52: STRONGBACKS
All or part of a shore may be used to make a strongback.
A strong back distributes pressure across a patch or shole.
Phase III VG 52

## Slide 53: STRONGBACK
Phase III VG 53

## Slide 54: TOOLS USED FOR SHORING
Sledge hammer
Crosscut saw
10’ and 50’ metal tape rule
Lumber crayon
Hatchet
Emergency light source
2 lbs of nails( 20d & 30 d )
Phase III VG 54

## Slide 55: TOOLS
Carpenter square
Shoring batten
Chain saw
Phase III VG 55

## Slide 56: SHORING STRUCTURES
Direct Compression - Strongest, easiest, and quickest structure to erect.
Triangular/Triangulation - Second best structure takes time to build. make sure the legs of the shoring are set between 45 and 90 degrees.
Phase III VG 56

## Slide 57
Phase III VG 57

## Slide 58: BREAK TIME
Phase III VG 58

## Slide 59: LOOSE WATER
Water with a free surface.
Phase III VG 59

## Slide 60: SOLID WATER
flooded compartment
Phase III VG 60

## Slide 61: NOTE
Compartments must be dewatered in a manner that will contribute to the overall stability of the ship.
Phase III VG 61

## Slide 62: DEWATERING PUMPS
Fixed bilge pump
P-250 portable pump
Phase III VG 62

## Slide 63: FIXED BILGE PUMPS
Will pump water directly overboard
Phase III VG 63

## Slide 64: P-250 PORTABLE PUMP
Has A 250 gpm rating.
Self priming lift of 16 - 20 ft.
Two stroke/ two cycle engine.
5oz of oil per gallon of gas.
Do not run more than 45 seconds without pressure on the gauge.
Phase III VG 64

## Slide 65: PMCS
Performed by engineers.
Run 10-15 min. weekly during emergency drills.
Keep tank full to prevent condensation.
Boatswain ensures task is completed.
Phase III VG 65

## Slide 66: DAMAGE CONTROL
Phase III VG 66